Rocket Science and Technology      4363 Motor Ave., Culver City, CA  90232

Phone: (310) 839-8956   Fax: (310) 839-8855

The Pitch-Yaw Wave Number (rev.3)             05 January 2013

by C.P.Hoult

Introduction

Most of you have heard me speak about the pitch/yaw wave number, and your eyes just glaze over when you hear that phrase.  What sort of techno-mumbo-jumbo can that be? you’re thinking.  Here’s the answer:

Discussion

First, our rockets are all more or less symmetric around their roll axes.  Their pitch moments of inertia are the same as their yaw moments of inertia.  And, the aerodynamic torques about the pitch axis are the same as about their yaw axis.

Now, imagine a rocket model suspended horizontally by a pitch axle passing through the center of gravity.  The rocket model is free to rotate about the pitch axis (passing through the center of gravity).

Now, imagine the model in a wind tunnel.  Further, suppose you reached in and tweaked the nose such that the model would freely oscillate.  Then, the differential equation describing the oscillations is

,

where   =  Pitch moment of inertia,

Pitch/yaw wave length,

=  Rocket length,

=  Time,

=  Atmospheric mass density,

=  Reference area for aerodynamic coefficients, body cross section area

=  Reference length for aerodynamic moment coefficients, body diameter

= Airspeed

=  Slope of pitch moment coefficient with respect to angle of attack, and

= Angle of attack.

To solve this differential equation, substitute

After a bit of math, you will find that

The quantity  is called the pitch natural frequency, and, as already noted, due to symmetry about the roll axis, it is the same as the yaw natural frequency.

The pitch period  is the time required for one complete pitch oscillation…that is, the time for  to go through 2π radians, or

But, during one oscillation period, the rocket will have moved through the air a distance

.  This distance  is the pitch wavelength.  After a little more math you’ll find that

Don’t worry about the minus sign;  is a negative number for a stable rocket.

The pitch wave number is a kind of frequency in the spatial domain instead of the time domain.  Instead of radians per second its units are radians per foot (or meter).  Numerically it’s just

Finally, and most remarkably, the same formula holds when  is not a constant, but is increasing under constant acceleration.  Trust me.  Even better, check it out yourself!

Finally, consider how the pitch wavelength scales with rocket size.  Imagine two rockets, one scaled up from the other.  In the equation for wavelength some parameters are not scale dependent.  These are density  , and .  However,  will be proportional to  and  is proportional to  because the mass is proportional to and the radius of gyration is proportional to .  Putting this all together,

.

In other words, bigger rockets have longer pitch/yaw wavelengths.

# Text boxes

U