Rocket Science and Technology      4363 Motor Ave., Culver City, CA  90232

Phone: (310) 839-8956   Fax: (310) 839-8855

Effects of Fin Static Aeroelasticity on Roll Rate  05 October 2013

by C. P. Hoult

Introduction

Thin fins are commonly flown on small sounding rockets.  The airfoils used can be simple Al plate or they can be built up by wrapping carbon fiber around a foam core.  This memo addresses the effects of subsonic static aeroelastic twisting on roll rate.  The motivation is the roll rate profile for CSULB's P-18 D rocket as shown in Fig. 1.  Here the roll rate starts to accelerate a few seconds prior to the failure at pitch-roll resonance.  The question that motivated this study is whether or not this increase was due to fin static aeroelasticity.  This memo documents the Excel™ code, TWISTIT.xls used to answer this question.

Figure 1   P-18 Flight test data

Nomenclature

_______Mnemonic_____________Definition________________________________

Parameters in the fin chord vs. spanwise coordinate relation

Fin semi span, ft from body centerline

Rolling moment coefficient

Roll damping moment coefficient

_______Mnemonic_____________Definition________________________________

Roll driving moment coefficient

Fin average airfoil normal force coefficient slope, rad-1

Constants of integration

Local fin chord, ft

Root chord, ft

Tip chord, ft

Torsional modulus of elasticity of the fin material, lb/ft2

Torsional stiffness of a fin airfoil, ft4

Rolling moment, ft-lb

Number of fin panels

Roll rate, rad/sec

Functions in the torsional solutions

Dynamic pressure, lb/ft2

Body radius, ft

Aerodynamic reference area, ft2

Torque about the elastic axis, ft-lb

Total fin thickness, ft

Flight speed, ft/sec

Fin skin thickness, ft

Distance from center line to a fin strip, ft

Local angle of attack, rad

Cant angle of a single fin panel, rad

Torsional deflection (twist angle), rad

Analysis

First, the assumptions:  The fin planform is assumed to be a clipped delta as sketched.  Next, the Mach number is subsonic.  The phenomena discussed here tend to be much less noticeable at supersonic speeds because there the airfoil center of pressure and elastic axis are much closer.  All angles of attack are small compared to unity.  The fin airfoil shape can be modeled as a flat plate.  As is customary, the roll moment of inertia is negligibly small.

The simplified aerodynamic model used here is strip theory.  In this approach the local normal force coefficient slope is approximated by an average taken over the entire planform.  Considering the very approximate nature of the elastic twisting model employed, it does not seem worthwhile to expend much effort on refining the airload distribution.

It is common to assert that designers choose fin sweep back to reduce fin wave drag or to increase critical Mach number.  In truth, it must be chosen to mitigate the possibility of a static aeroelastic failure due to chordwise curling of the leading edge in the tip region.  It is assumed that the fin is swept back sufficiently to preclude chordwise bending; it can therefore be neglected.  Swept fins are also known for coupling between torsion and spanwise bending.  It is assumed that static bending-torsion coupling can be neglected because the coupling effects of fin cant and roll damping are approximately equal, but of opposite sign.

The elastic model used considers the fin to be a slender beam of high aspect ratio.  Results reported in ref.(2) indicate that the slender beam approximation will overestimate the torsion deflection by about 20%.  However, all we are trying to do is provide the designer with a tool that indicates trends.  For that purpose this error is acceptable.  	Figure 2 below displays the fin geometry:

Figure 2  Fin Geometry

Torsional Deflections

Consider the fin to be a one-dimensional beam subject to torsional deformations.  Assume the elastic axis lies on the fin half chord line.  Since subsonic flow has been assumed, the aerodynamic loading will be centered on the quarter chord line as sketched in Fig. 2.  The air loads of interest are due to torsion, cant angle, roll damping and angle of attack.  Then, the torque about the elastic axis from a strip of fin will be:

(1)

The change in twist angle over the strip is given by the St. Venant theory

(2)

Torsional Stiffness

There are two kinds of fin structure to be considered:  First, a solid plate for which

.                                                       (3a)

Second, a built-up structure for which thin skins of thicknessare laid up on a foam or balsa core to form a flat plate airfoil.  Neglecting the contribution of the core leads to  Bredt's formula for the torsional stiffness:

(3b)

Note that the chord varies with the spanwise coordinate according to:

(4)

Putting these pieces together gives

(5a)

For a straight-tapered planform, we can change the independent variable from to :

(5b)

where                                                                                       (5c)

The initial conditions for a root chord clamped to the body are:

, and                                                     (6a)

@  , or

(6b)

Equations (5) have a general solution in terms of modified Bessel functions of the first kind and of fractional order.  However Excel™ only supports I functions whose order is a positive integer.  Therefore, recourse to numerical methods will be taken.

Because the  response is proportional to the appropriate right hand side, each of the three  solutions takes the form

(8)

Then, the functions A,  and  can be found numerically integrating:

(9)

subject to the initial conditions ( eq's. (6) )

Loads Acting on a Flexible Fin

Now, suppose we knew the three solutions, ,  and .  We next show how to find the "elasticized" loading.  Consider the angle of attack response on a strip of span dy.  The rigid fin  remains the same as always.  But, aeroelastic effects increase  by

,                                       (10a)

and the corresponding increment in is

.                                        (10b)

Futhermore, there is an change to the normal force, including upwash around the body, acting on a fin panel

.                                         (10c)

Thus, integrate eq's. (9) , and at the same time, evaluate eq's. (10) as auxiliary integrals.  Use eq. (4) to relate  and .

Roll Equilibrium

Roll equilibrium is achieved when the two roll torques are in balance.  First, recapitulate the rigid fin strip theory for  and .  Consider a strip of span for which

d(Roll damping moment).

Then, roll damping moment

Then, for one fin panel

(11a)

d(Roll driving moment).  And, for one fin panel,

(11b)

The full stability derivatives are the sum of eq's. (10) and (11).  The equilibrium spin rate is estimated by setting sum of all the roll moments equal to zero, and solving for the roll rate.  Then, if all fin panels have the same cant angle,

(12)

Equation (12), with its aeroelastic corrections, can be used to predict roll rate given fin cant angles, or vice versa.

Results

The model described above has been coded into Excel™ and filed as TWISTIT.xls. For typical numbers, data for P-18D was used, and the results for ,  and plotted below:

| Parameter | Value |
| --- | --- |
| Root chord | 24" |
| Tip chord | 4" |
| Body Radius | 12.5" |
| Fin semispan from body centerline | 39.6" |
| Fin total thickness | 0.375" |
| Fin skin thickness | 0.02742" |
| Fin J/c | 0.00771 in3 |
| Dynamic pressure | 800 psf |

The following table summarizes the results:

| Parameter | CL | CLp |
| --- | --- | --- |
| Rigid | 2.399 | -4.808 |
| Flexible increment | 4.426 | -6.141 |
| Total | 6.825 | -10.949 |

We immediately discover that the flexible fin roll rate is 25% greater than its rigid counterpart.   The general dependence of the flexible roll rate to rigid roll rate ratio on dynamic pressure is shown below.  Note that the maximum dynamic pressure observed during the P-18D flight was only 673 lb/ft2.

Summary

This very approximate analysis shows that fin static aeroelasticity effects probably operated to increase the P-18D roll rate beyond its rigid fin value, but most likely there is an additional cause to the increase in roll rate observed near failure.

- F. B. Hildebrand, "Advanced Calculus for Engineers", Prentice-Hall, Inc.,  New York, 1949

- R. L. Bisplinghoff, H. Ashley and R. L. Halfman, "Aeroelasticity", Addison-Wesley Publishing Company, Cambridge, 1956

# Footnotes

A more accurate approximation is  (1  ̶  0.63t/c).  In most practical cases, the two formulae differ by only a few percent.

# Text boxes

b

cT

cR

Aerodynamic Centers

R

Strip

y

Elastic Axis